## Slide 1: Ne2K Gas Energy Resolution Measurement at BNL (I)
B.Azmoun, BNL

## Slide 2
WIS SetUp
WIS energy resolution in Ne2K gas ~24%(sigma)
BNL will repeat measurement for verification
140um pitch
280um pitch
280um pitch
140um pitch

## Slide 3
Ne2K gas (Ne-CF4-iC4H10 95/3/2), Flow = 1.4slpm(insures high purity), Press.~atm. (low impedance), Temp=22C
4GEM(All): Std. CERN Cu 4-way segmented foils; pitch-inner/outer hole: 140-50/70 um (we do not have 280um pitch GEMs) [See details of GEM config. in spreadsheet]
COMPASS Readout (grounded)
Collected charge from bottom electrode of bottom GEM
Used Fe55 flood source, no collimation
Read out using histogram feature of scope (good zero crossing; no time slew)
BNL SetUp
Drift Gap: 13.2mm, 0.4kV/cm
Transfer 1: 1.6mm, 0.5kV/cm
Induction: 2.9mm, 2.3kV/cm
Transfer 3: 1.6mm,, 0.05kV/cm
GEM 2
GEM 3
GEM 4
Mesh
X-Y Strips
Preamp/Shaper
Connected to bot. GEM
Transfer 2: 1.6mm, 0.5kV/cm
Fe55 flood source
GEM 1
Microscope pics of BNL GEMs
(image is hazy since GEMs are inside plastic bag for protection)
~Hole Size
~Hole Pitch

## Slide 4: Data Taking
180, 200, 250, 295V
180, 200, 250, 275V
Conversions
in TG1
Conversions
in DG
Eyeball Estimate
Normal Mode used for data taking
Fast Acquisition Mode used for diagnostics

## Slide 5: Fit histos
Res(sigma) = 9.4%
Res(sigma) = 10.3%
180, 200, 250, 295V
180, 200, 250, 300V
Preamp saturation
(Imported histo data into root for better estimate of resolution)

## Slide 6
Pedestsal
Didn’t unfold pedestal width from sigma of pulse height distributions since it’s negligible

## Slide 7: Remarks
Will repeat measurement once we get at least two 280um pitch foils, but for now we see approx. 10% (sigma) energy res.
Where do we get the 280um pitch foils?
Likely using 280um pitch foils for 2 inner GEMs will worsen the resolution, but by x2.5?, not sure…
  In the sketch of the WIS setup, it appears that an xray gun may have been used for the measurement (or maybe was left on inadvertently while using an Fe55 source); is it possible that the 24% sigma energy resolution measured by WIS has folded into it the full x-ray energy spectrum? (Long shot, but just in case…)